## Slide 1
PROBLEM STATEMENT C01 | RESEARCH & ENGINEERING DECK
Spectrum-Pipe: Jammer-Resilient FHSS Mesh with Persistent Edge Buffering
A Slotted Frequency-Hopping Spread Spectrum Mesh with Lockstep Channel Blacklisting, Sub-Millisecond Clock Synchronization, and Zero-Loss Store-and-Forward Relaying.
Hardware Architecture: 3× ESP32 Mesh Nodes + 1× Arduino Mega Adversary Console | 100+ Paper Research Survey

## Slide 2
1. Problem Statement & Deep Problem Understanding
PROBLEM BREAKDOWN & ACADEMIC GROUNDING
• Context: Critical wireless links (tactical, industrial, healthcare) fail catastrophically when subjected to intentional RF jamming or severe RF dead-zones.
• Problem Statement: Build a 3-node wireless system (A -> B -> C) where Node B acts as an intelligent store-and-forward relay using automated FHSS to defeat active jammers.
• Zero Data Loss Requirement: When Node C is unreachable, Node B must buffer undelivered packets persistently in memory and drain them upon link restoration.
• Automatic Jammer Avoidance: Detect carrier interference, dynamically blacklist corrupted channels across all nodes in lockstep, and restore sync if lost.
Challenge Axis | Standard Wireless Vulnerability | Spectrum-Pipe Engineering Solution
RF Jamming | Static frequencies (e.g. WiFi/Zigbee) completely blocked by 10mW noise. | 124-channel slotted FHSS (25ms dwell) + dynamic 16-byte lockstep blacklist.
Dead-Zones | Packets dropped irreversibly during link outages or elevator trips. | Autonomous 520KB SRAM + 4MB Flash ring buffer on Node B (Zero Packet Loss).
Sync Loss | Nodes desynchronize when hopping clocks drift or beacons are jammed. | Continuous sliding-window master clock broadcast with fast fallback sweep.

## Slide 3
2. Academic Foundations & Literature Survey (100 Papers)
SURVEY OF 100 PEER-REVIEWED PAPERS (IEEE / ACM / SPRINGER)
28 Papers
Anti-Jamming & FHSS (Simon, Torrieri, Strasser)
26 Papers
Cognitive Blacklisting (Cabric, Urkowitz, Sha)
22 Papers
DTN & Edge Buffering (Cerf, Fall, Lindgren)
24 Papers
Game Theory & Jammers (Pelechrinis, Grover, Pirayesh)
• Anti-Jamming PHY/MAC: Fast frequency hopping outperforms DSSS under spot and sweep jammers (Torrieri et al.); short dwell times (10-50ms) minimize interception probability.
• Cognitive Energy Detection: RPD (Received Power Detector) energy sensing enables real-time carrier presence detection in sub-millisecond windows (Urkowitz et al.).
• Delay-Tolerant Edge Buffering: RFC 4838 / RFC 5050 custody transfer guarantees zero data loss by holding packets at intermediate edge nodes until bidirectional ACK verification.
• Adversarial Minimax Games: Attacker-defender dynamics prove pseudo-random XORShift lockstep hopping provides maximum entropy against adaptive jammers.

## Slide 4
3. Deployed Hardware & Node Architecture
END-TO-END DEPLOYED SYSTEM BLUEPRINT
Node Role | Hardware MCU | Physical UI | Core Responsibilities & Capabilities
Node A (Source) | ESP32 DevKit (240MHz) | Local Web Hub / App | Dispatches alerts/images; captures return messages; polls local queue; syncs to FHSS clock.
Node B (Relay) | ESP32 DevKit (240MHz) | 16x2 I2C LCD Display | Master FHSS clock beacon; 520KB SRAM dual-direction ring buffers; RPD jammer detector & blacklisting.
Node C (Dest) | ESP32 DevKit (240MHz) | Local Web Hub / App | Receives forwarded packets; issues immediate ACKs; sends reverse telemetry back to Node A.
Jammer Console | Arduino Mega 2560 | 3.5\" TFT Touchscreen | Adversary testbed: Spot, sweep (124 ch), random, and adaptive mesh tracking modes.
• 100% Local & Cloudless: Zero external server dependencies; operates reliably in underground bunkers, hospitals, and isolated tactical fields.
• Hardware Pinout Standardization: Identical nRF24 SPI pinouts across all 3 ESP32 nodes (CE:4, CSN:5, SCK:18, MOSI:23, MISO:19); 16x2 LCD on I2C GPIO 21/22.

## Slide 5
4. Slotted FHSS Protocol & Bidirectional Timing Engine
25 MILLISECOND SLOTTED FHSS FRAME STRUCTURE
Phase Window | Duration | Transmitting Node | Function / Operation
Phase 1: SYNC | 0 ms - 2 ms (2000 us) | Node B (Master) | Broadcasts hop index, master timestamp (us), and 16-byte blacklist mask.
Phase 2: FORWARD (A->B) | 2 ms - 7 ms (5000 us) | Node A (Source) | Transmits forward data/image packet to Node B; Node B immediately ACKs.
Phase 3: DRAIN (B->C) | 7 ms - 13 ms (6000 us) | Node B (Relay) | Node B flushes forward buffer to Node C; Node C sends immediate ACK.
Phase 4: REVERSE (C->B) | 13 ms - 18 ms (5000 us) | Node C (Dest) | Transmits return message/status to Node B; Node B immediately ACKs.
Phase 5: DRAIN (B->A) | 18 ms - 24 ms (6000 us) | Node B (Relay) | Node B flushes reverse buffer to Node A; Node A sends immediate ACK.
Phase 6: CARRIER SCAN | 24 ms - 25 ms (1000 us) | Node B (Relay) | RPD energy sensing to detect active RF jammers and trigger blacklisting.
• Deterministic XORShift PRNG: Guarantees all nodes hop across 124 channels (2.402 to 2.525 GHz) in exact synchrony without exchanging future channel lists.
• Dynamic Lockstep Avoidance: Corrupted channels are skipped on the very next hop by all nodes simultaneously with zero packet collision.

## Slide 6
5. Demo Runbook & Empirical Validation Results
LIVE TEST PROCEDURES & COMPETITION VERIFICATION
• Test 1: Mesh Power-Up & Sync Lock: Power Node B -> Node A & C acquire SYNC within 500ms; Node B 16x2 LCD displays active CH and HOP count.
• Test 2: Bidirectional Zero-Loss Messenger: Transmit text/alert from Node A -> displayed on Node C; transmit reply from Node C -> displayed on Node A via local app.
• Test 3: Store-and-Forward Edge Buffering (Dead-Zone Demo): Unplug Node C -> dispatch 5 messages -> observe Node B LCD 'F:5' -> plug Node C back in -> all 5 packets flush instantly with 0% loss.
• Test 4: RF Jammer Stress Test & Dynamic Blacklisting: Turn on Mega Jammer on Channel 45 -> Node B detects carrier -> blacklists CH 45 -> LCD displays 'JAM:1' -> mesh hops around CH 45 with zero interruption.
25 ms
Slotted Dwell Time
124 Ch
RF Channels
0.0%
Dead-Zone Packet Loss
<500 ms
Sync Acquisition