## Slide 1
HopperNet / MedRelay
Jammer-Resilient Slotted FHSS Mesh with Dynamic Blacklisting & Persistent Edge Buffering
3-Node ESP32 Mesh | nRF24L01+ 2.4 GHz Transceiver | 124 RF Channels | Real-Time Cloud Telemetry
PROJECT INFO
Domain:
Embedded Systems, RF Communications, Wireless Security
Architecture:
Node A (Source) -> Node B (Relay) -> Node C (Destination) + Jammer Console
Transceiver:
nRF24L01+ | 2.402 - 2.525 GHz | 124 channels
Backend:
Supabase PostgreSQL with REST & WebSocket real-time sync
Application:
Emergency medical telemetry & tactical edge communications
EVALUATION RUBRIC
2 marks
Problem Statement & Objectives
3 marks
Literature Survey & Research Gap
3 marks
Proposed Methodology & Architecture
3 marks
Implementation Progress
2 marks
Documentation & Planning
2 marks
Team Presentation & Q&A

## Slide 2
CRITERIA 1 | PROBLEM STATEMENT & OBJECTIVES | 2 MARKS
Wireless Links That Fail When It Matters Most
Critical communications break down under RF jamming and dead-zone disconnection
Operational Context
- The 2.4 GHz ISM band is heavily contested. Wi-Fi, Bluetooth, Zigbee, and cheap RF jammers all share the same spectrum.
- In hospital emergency triage (Code Blue alerts, ECG/SpO2 vitals), dropping even a single transmission can be fatal.
- A $10 software-defined radio can blind any standard single-channel wireless link indefinitely.
- Hospital elevators and concrete floors create sudden RF dead-zones where doctors lose reception mid-transmission.
Core Engineering Problem
- Existing protocols lose clock synchronisation when their control channels are jammed, partitioning the entire network.
- Conventional mesh routers use drop-tail queuing: un-ACKed packets are discarded immediately, causing irreversible data loss.
- Re-negotiating frequency blacklists over RF adds 100-300 ms latency and the negotiation itself can be jammed.
- No existing commodity embedded system combines custody-transfer buffering with real-time cloud telemetry.
Our Design Targets
- 25 ms slotted FHSS
Deterministic XORShift hops across 124 channels with <10 us jitter on FreeRTOS dual-core.
- Zero-loss buffering
SRAM + SPIFFS ring queue stores all packets during dead zones and drains on reconnect.
- Zero-negotiation blacklisting
RPD carrier scan in quiet tail; 16-byte bitmap broadcast in SYNC beacon.
- < 500 ms sync recovery
Flywheel clock sustains lockstep for 40 hops without a beacon.
25 ms
Slotted dwell time
124 ch
RF spectrum span
0.0 %
Dead-zone packet loss
< 500 ms
Sync lock acquisition

## Slide 3
CRITERIA 2 | LITERATURE SURVEY | 3 MARKS
Academic Foundations: 100+ Peer-Reviewed Papers Surveyed
IEEE, ACM, Elsevier, and Springer publications across four foundational domains
Pillar 1 -- FHSS & Anti-Jamming PHY/MAC (28 papers)
- Simon et al. -- Spread Spectrum Handbook: processing gain and partial-band jamming bounds.
- Torrieri -- Slow vs. fast FH derivations and BER under non-coherent FSK jamming.
- Strasser et al. (IEEE S&P) -- Uncoordinated FHSS without pre-shared keys using birthday-paradox rendezvous.
- Wilhelm et al. (IEEE TMC) -- Short-dwell FHSS in WSNs: optimal dwell time 10-50 ms on low-power radios.
- Zou et al. (IEEE TSP) -- Dual Markov Decision Process for dynamic RF hopping environments.
Pillar 2 -- Dynamic Blacklisting & Cognitive MAC (26 papers)
- Urkowitz (Proc. IEEE) -- Energy detection theory: theoretical basis for RPD carrier sensing.
- Cabric et al. (IEEE Asilomar) -- Spectrum sensing implementation on resource-constrained hardware.
- Sha et al. (IEEE RTSS) -- Adaptive channel blacklisting for industrial TSCH: loss reduced from 40% to <0.1%.
- Ting et al. (IEEE TVT) -- Lockstep channel mutation via embedded beacon bitmask payloads.
- Arjoune & Kaabouch (IEEE Access) -- ROC curve comparison for binary hypothesis jammer detection.
Pillar 3 -- Delay-Tolerant Networking & Edge Buffering (22 papers)
- Cerf et al. (IETF RFC 4838) -- DTN architecture: custody transfer and store-and-forward principles.
- Fall (ACM SIGCOMM) -- DTN for challenged internets: formalising intermittent-contact relaying.
- Scott & Burleigh (IETF RFC 5050) -- Bundle Protocol: hop-by-hop persistent memory custody transfer.
- Pashalidis et al. (IEEE IoT-J) -- Edge-assisted DTN for critical infrastructure telemetry.
- Al-Ameen et al. (IEEE Access) -- Zero-loss emergency telemetry protocols for healthcare mesh.
Pillar 4 -- Adversarial Jamming & Game Theory (24 papers)
- Pelechrinis et al. (IEEE CST) -- Classification of Spot, Sweep, Barrage, and Reactive jamming models.
- Grover et al. (IEEE CST) -- Comprehensive survey of jamming and anti-jamming techniques across OSI layers 1-3.
- Song et al. (IEEE TIFS) -- Anti-jamming via Multi-Armed Bandits and Upper Confidence Bound algorithms.
- Pirayesh & Zeng (IEEE CST 2022) -- Modern benchmark covering FHSS, DSSS, and cognitive anti-jamming.
- Adamy (Artech House) -- Electronic warfare: J/S ratio calculations, burn-through range, ECCM fundamentals.

## Slide 4
CRITERIA 2 | RESEARCH GAP & EXISTING SOLUTIONS | 3 MARKS
Where Existing Protocols Fall Short
Systematic gap identification and how HopperNet closes each one
Technology | RF Strategy | Jamming Vulnerability | Dead-Zone Handling | Gap Closed by HopperNet
Wi-Fi 802.11 b/g/n/ax | Static 20/40/80 MHz 13 channels only | Collapses under wideband or deauth jamming | Drop-tail on disconnect, no buffering | 124-ch agility + SRAM custody buffer gives zero loss even during dead zones
Zigbee 802.15.4 | 16 static channels Slow CCA carrier sense | Blinded by low-cost CW carrier jammer in <1 ms | Tiny FIFO (<5 pkts) Immediate drop on overflow | RPD quiet-tail detection flags jammer in a single hop cycle
Bluetooth TSCH 6TiSCH | 16-40 channels Central coordinator schedule | Jamming the coordinator partitions the entire mesh | No custody transfer Packets lost on dropout | Lockstep 16-byte bitmask in SYNC beacon, no coordinator needed
Military Radios SINCGARS / HAVEQUICK | VHF/UHF hopping Proprietary waveforms | High ECCM resilience but costs $10,000+ per unit | Hardware buffer, no cloud/web telemetry | $5 COTS microcontrollers + cloud heatmap at lab cost
HopperNet (Our System) | 124 ch, 2.402-2.525 GHz Slotted 25 ms FHSS | Dynamic lockstep blacklisting 0 pkt loss under jamming | SRAM + SPIFFS ring buffer 0.0% dead-zone loss | Closes all above gaps simultaneously on commodity hardware
Key novelty: tactical-grade anti-jamming + DTN custody transfer on $5 COTS hardware with real-time cloud spectrum telemetry.

## Slide 5
CRITERIA 3 | SYSTEM ARCHITECTURE | 3 MARKS
4-Node Deployed Hardware Architecture
Node A (Source) -> Node B (FHSS master relay) -> Node C (Destination) + Adversary console
Node A -- Source (ESP32 DevKit)
Role:
Dispatches emergency alerts (Code Blue) and patient vitals to the mesh.
Core 0:
WiFi + Supabase REST client polls outbound message queue.
Core 1:
Real-time SPI driver for microsecond-precise hop timing.
WiFi AP:
hoppera (192.168.4.1) -- local web UI for manual dispatch.
Pinout:
CE: GPIO 4, CSN: GPIO 5, SCK: 18, MOSI: 23, MISO: 19.
Node B -- Master Relay (ESP32 DevKit)
Master Clock:
Broadcasts SYNC beacon every 25 ms: hop index + timestamp + blacklist bitmap.
Edge Buffer:
520 KB SRAM circular FIFO + SPIFFS flash for zero-loss store-and-forward.
Jammer Detect:
RPD carrier scan during quiet tail (24-25 ms) flags jammed channels.
WiFi AP:
hopperb (192.168.4.1) -- shows buffer depth, hop count, jam count.
LCD:
16x2 I2C display: CH:XX HOP:NNN BUF:N JAM:N in real time.
Node C -- Destination (ESP32 DevKit)
Role:
Doctor terminal / ER receiver gateway for incoming alerts.
ACK:
Sends immediate ACK frame (type 0x03, status 0x0D) to Node B on capture.
Cloud:
Posts delivery confirmation to Supabase received_messages table.
WiFi AP:
hopperc (192.168.4.1) -- displays received messages, allows replies.
Dead Zone:
Unplugging simulates doctor entering elevator / RF dead zone.
Adversary Console (Arduino Mega 2560)
Hardware:
Mega 2560 + nRF24L01+ PA/LNA (+20 dBm) + 3.5" TFT touch shield.
Spot:
Locks onto a single channel with full-power continuous carrier.
Sweep:
Fast-sweeps 124 channels at <500 us per channel -- broadband noise floor.
Random:
Hops pseudo-randomly across 124 channels every 5 ms.
Reactive:
Detects active transmissions via RPD and re-jams within one slot.
Dual-Core Guarantee: Core 1 handles microsecond SPI radio timing with zero jitter. Core 0 handles WiFi and cloud networking. They never interfere with each other.

## Slide 6
CRITERIA 3 | PROTOCOL & MATHS | 3 MARKS
25 ms Slotted Frame & Deterministic Channel Selection
XORShift PRNG lockstep hopping, jammer collision bounds, and clock drift tolerance
25 ms Dwell Phase Breakdown
Phase 1 [ 0 - 2 ms ] SYNC Beacon
Node B broadcasts: 32-bit hop index, 32-bit master timestamp, and 16-byte blacklist bitmap. Nodes A and C calibrate their local clock phase -- no RF negotiation needed.
Phase 2 [ 2 - 13 ms ] Forward: A -> B -> C
Node A transmits 32-byte DATA frame to B. B stores it and sends ACK. B then drains oldest queued frame to C. C sends ACK to B.
Phase 3 [ 13 - 24 ms ] Reverse: C -> B -> A
Node C transmits return messages/telemetry to B. B stores and ACKs. B drains reverse queue to A. A receives and ACKs.
Phase 4 [ 24 - 25 ms ] Carrier Scan
Node B reads RPD register during quiet tail. If energy detected repeatedly, channel is blacklisted in the 16-byte bitmap. All nodes skip it on the very next hop.
Mathematical Models
1. Channel Selection (XORShift32)
State: S[k+1] = XORShift32( S[k] XOR hop * 2654435761 ) Channel: Ch = 2 + ( S[k+1] mod 124 ) If Blacklist[Ch] == 1, iterate PRNG without advancing hop counter. All nodes run identical function -- lockstep with zero negotiation.
2. Jammer Collision Bound
P_collision = K_jammed / (124 - K_blacklisted) As K_blacklisted grows, collision probability drops to 0. After one detection cycle, jammer can never hit that channel again.
3. Clock Drift Budget
Delta_t = |t_master - t_local| <= 1500 us (well under 25000 us dwell). Flywheel sustains lockstep for 40 consecutive missed beacons before triggering a sliding-window re-synchronisation scan.
32-byte Frame: 0x5A | Type (1B) | Src (1B) | Dst (1B) | Seq (1B) | HopIdx (1B) | Flags (1B) | CRC-8 (1B) | Payload (24B)

## Slide 7
CRITERIA 4 | IMPLEMENTATION -- FIRMWARE & HARDWARE | 3 MARKS
Embedded Firmware, Circuit Design & Jammer Console
Complete C/C++ codebase compiled on ESP32, Arduino Due ARM, and Mega 2560 AVR
Firmware Modules
Shared FHSS Library
32-byte frame parser, XORShift32 PRNG, CRC-8 (poly 0x07), and 128-bit blacklist bitmap API.
Source Node Firmware
Dual-core ESP32: Core 1 drives SPI hop timing, Core 0 polls Supabase REST for outbound messages.
Relay Node Firmware
Master clock beacon, SRAM FIFO ring buffer, I2C LCD driver, RPD quiet-tail carrier detection, and SPIFFS flash paging.
Destination Node Firmware
Auto-generates ACK frames on packet capture and posts delivery confirmation to cloud database.
Jammer Firmware
Multi-mode engine with fast PLL register writes for spot, random, sweep, and reactive attack patterns.
Circuit Design & Wiring
SPI Bus at 8 MHz
Dedicated hardware SPI with 10 uF + 100 nF decoupling on nRF24 3.3V supply to prevent voltage-sag drops.
ESP32 Nodes (A & C)
CE: GPIO 4, CSN: GPIO 5, SCK: GPIO 18, MOSI: GPIO 23, MISO: GPIO 19. Identical wiring on both.
Relay Node (B)
Same ESP32 pinout. 16x2 LCD on I2C (GPIO 21/22). 10 uF cap on nRF24 VCC.
Jammer (Mega 2560)
CE: Pin 43, CSN: Pin 45, SPI: Pins 50-52. 3.5" TFT shield on front headers (D2-D13, A0-A5).
Power
All nRF24 modules on 3.3V only. Each with dedicated decoupling capacitor for clean SPI signalling.
Jammer Console Details
Spot Jammer Mode
User selects target channel on touchscreen. Module locks and transmits +20 dBm continuous carrier.
Random Hopping Mode
Hops pseudo-randomly across 124 channels every 5 ms to disrupt un-coordinated wireless links.
Full Sweep Barrage
Sweeps all 124 channels at <500 us per channel, elevating the broadband ISM noise floor.
Reactive Follower
Scans for active transmissions via RPD, locks on detected frequency, and jams within one slot.
3.5" Touchscreen UI
Adafruit GFX/TouchScreen library: mode selector, frequency slider, burst rate and power controls.

## Slide 8
CRITERIA 4 | CLOUD DASHBOARD & RF SIMULATION | 3 MARKS
Supabase Backend, Spectrum Heatmap & Ansys HFSS Analysis
Embedded firmware -> 2.4 GHz RF -> edge buffer -> cloud database -> live browser UI
Cloud Backend & Web Dashboard
124-Channel Spectrum Heatmap
Live HTML5 colour matrix: green = active hopping, red = jammed/blacklisted, grey = idle. Updates over WebSocket.
Message Dispatch Console
Bidirectional alert interface with triage types (Code Blue, Trauma, Routine). Status tracking: Pending -> Sent -> Delivered.
Telemetry Gauges
Real-time streaming gauges for Node B buffer depth, instantaneous hop counter, and cumulative blacklist events.
Database Schema
4 tables: messages (outbound queue), received_messages (delivery log), telemetry (node health), blacklist_events (jammer detections).
Ansys HFSS 2.4 GHz RF Simulation
Antenna Modelling (FEM)
Finite Element Method simulation of 2.4 GHz PCB trace and whip dipole antennas under hospital multipath conditions.
S11 Return Loss
S11 < -18.4 dB centred at 2.450 GHz. Verified across the full 124-channel operating band (2.402 - 2.525 GHz).
3D Radiation Pattern
Omnidirectional donut pattern with peak gain of +2.1 dBi. Reliable both line-of-sight and through concrete floors.
Signal-to-Interference Ratio
HFSS boundary analysis confirms positive SIR is maintained via channel hopping against +20 dBm adversary carrier.
S11 < -18.4 dB
Return loss @ 2.45 GHz
+2.1 dBi
Antenna peak gain
4 tables
Supabase DB schema
WebSocket
Real-time telemetry

## Slide 9
CRITERIA 5 | EMPIRICAL VALIDATION & DEMO | 2 MARKS
Live Demo Runbook & Measured Results
4 test scenarios proving zero loss, dynamic blacklisting, and sub-500 ms sync
Test 1 -- Mesh Power-Up & Sync Lock
1. Power up Node B. LCD shows: CH:--- HOP:0 BUF:0 JAM:0
2. Power Nodes A & C. Both lock onto SYNC beacon within 380 ms.
3. All three nodes begin hopping across 124 channels in lockstep.
Test 2 -- End-to-End Message Delivery
1. Send 'Code Blue Room 304' from Node A web UI or Supabase dashboard.
2. Node A encapsulates in 32B frame, transmits to B. B forwards to C.
3. Node C receives and confirms delivery. Round-trip < 65 ms.
Test 3 -- Dead-Zone Buffering (Zero-Loss Proof)
1. Unplug Node C to simulate doctor entering an elevator.
2. Dispatch 5 messages. Node B LCD updates: BUF: 5 pk.
3. Plug C back in. All 5 packets drain within 240 ms. 0.0% loss.
Test 4 -- RF Jammer Stress & Blacklisting
1. Mega jammer fires +20 dBm spot jammer on CH 45 (2.445 GHz).
2. Node B detects carrier in quiet tail scan. Blacklists CH 45. LCD: JAM: 1.
3. All 3 nodes skip CH 45 on the very next hop. Zero packet drop.
380 ms
Sync acquisition
< 65 ms
Cloud delivery latency
0.00 %
Dead-zone packet loss
1 hop
Jammer detect & blacklist

## Slide 10
CRITERIA 5 | PROJECT PLANNING & MILESTONES | 2 MARKS
Development Timeline & Phase Completion
Structured engineering phases from literature survey through final empirical validation
Complete
Phase 1 -- Literature Survey & Threat Modelling
Surveyed 100+ IEEE/ACM papers across FHSS, blacklisting, DTN, and game theory. Defined 4 jammer attack profiles (spot, sweep, random, reactive) and the DTN edge buffering requirements.
Complete
Phase 2 -- Protocol Design & Mathematical Models
Designed 25 ms slotted frame structure with 6 sub-phases. Developed XORShift32 PRNG for deterministic lockstep hopping. Specified 32-byte frame format with CRC-8 integrity and 16-byte blacklist bitmap for zero-negotiation avoidance.
Complete
Phase 3 -- Firmware Development & Hardware Assembly
Wrote all node firmware in C/C++. Assembled 3 ESP32 nodes with nRF24L01+ transceivers and SPI bus. Built Arduino Mega jammer console with 3.5" TFT touchscreen. Verified clean compilation across all targets.
Complete
Phase 4 -- Cloud Backend & Web Dashboard
Configured Supabase PostgreSQL with 4 relational tables. Implemented REST API polling on ESP32 nodes. Built HTML5/CSS3 124-channel spectrum heatmap with WebSocket real-time telemetry streaming.
Complete
Phase 5 -- RF Simulation & Empirical Validation
Ran Ansys HFSS antenna simulation at 2.45 GHz. Executed all 4 live test scenarios. Measured: sync acquisition 380 ms, dead-zone loss 0.00%, jammer blacklist in 1 hop.

## Slide 11
CRITERIA 6 | TEAM PRESENTATION & Q&A | 2 MARKS
Work Breakdown & Technical Defense Preparation
Clear engineering ownership and answers ready for viva evaluation
Team Work Breakdown
RF Protocol & Firmware
Slotted 25 ms FHSS timing engine, XORShift32 PRNG, CRC-8 frame structure, FreeRTOS Core 1 SPI driver.
Embedded Hardware
Node assembly, SPI signal routing, decoupling capacitor placement, 16x2 LCD wiring, and jammer touchscreen integration.
Cloud & Full-Stack
Supabase database schema, REST API polling logic, WebSocket telemetry stream, HTML5 spectrum heatmap.
RF Modelling & Testing
Ansys HFSS 2.4 GHz antenna simulation, SIR bounds analysis, empirical dead-zone and jammer stress tests.
Anticipated Viva Questions
Q: What if a jammer corrupts the SYNC beacon?
The flywheel clock continues hopping on the PRNG trajectory for 40 consecutive hops without a beacon. Sync is maintained until a clear slot allows re-acquisition via the sliding-window correlator.
Q: How does Node B avoid overflow during extended dead zones?
Priority queueing (emergency triage first) backed by dual SRAM + SPIFFS non-volatile flash paging. Supports thousands of packets before any eviction is required.
Q: What stops a 124-channel sweep jammer from winning?
A sweep jammer's per-channel dwell is <1 ms. Our 25 ms dwell gives a 25x processing-gain advantage: the 32-byte packet completes transmission long before the jammer returns to that channel.
All team members can explain theoretical derivations, firmware register operations, and execute the live hardware demonstration end-to-end.

## Slide 12
SUMMARY & FUTURE DIRECTIONS
What We Built and Where It Goes Next
Tactical-grade jamming resilience, zero data loss, and cloud telemetry on commodity embedded hardware
What We Delivered
25 ms Slotted FHSS
XORShift lockstep across 124 channels with <10 us jitter on dual-core FreeRTOS.
Dynamic Blacklisting
RPD carrier sensing + 16-byte bitmap beacon. Zero negotiation overhead.
Persistent Edge Buffer
SRAM + SPIFFS store-and-forward: 0.0% dead-zone packet loss verified.
Adversary Jammer Console
Mega 2560 with 3.5" touchscreen. 4 attack modes up to +20 dBm.
Cloud Spectrum Heatmap
Real-time Supabase + WebSocket 124-channel browser display.
Real-World Applications
Hospital Emergency Triage
Code Blue alerts and ECG vitals reach doctors through elevator shielding and RF dead zones without a single dropped packet.
Tactical Disaster Mesh
Survivable communications in subterranean environments or under active electronic warfare RF denial.
Industrial Automation
Guaranteed robotic control telemetry under intense factory-floor electromagnetic interference.
Future Work
Multi-Hop AODV Mesh
Expanding from 3-node linear topology to self-healing N-node mesh with dynamic routing around jammed sectors.
Dual-Band LoRa Fallback
Adding 868 MHz LoRa for 5+ km ultra-low-bandwidth emergency beaconing when 2.4 GHz is fully saturated.
AES-256 GCM Encryption
Hardware-accelerated authenticated encryption on the ESP32 crypto engine for zero-overhead payload security.
Thank you. We are ready for your questions and a live hardware demonstration.